Marantz 2250B Capacitor List

Power Amplifiers (Need 2 of each)

- C701 - 3.3µF 25V polar electrolytic

  - WIMA 3.3µF 50V MPF capacitor

- C702 - 10µF 35V polar electrolytic

  - Elna Silmic II 10µF 50V 604-1119-ND

- C704 - 47µF 50V polar electrolytic

  - Elna Silmic II 47µF 100V 604-1107-ND

- C705 - 47µF 16V polar electrolytic

  - Elna Silmic II 47µF 25V 604-1054-ND

- C706 - 220µF 50V polar electrolytic

  - Elna Silmic II 220µF 100V 604-1102-ND

Power Supply

- C801 - 220µF 63V polar electrolytic

  - Elna Silmic II 220µF 100V 604-1102-ND

- C802 - 100µF 50V polar electrolytic

  - Elna Silmic II 100µF 50V 604-1120-ND

- C804 - 22µF 35V polar electrolytic

  - Elna Silmic II 22µF 50V 604-1122-ND

- C805 - 330µF 50V polar electrolytic

  - Elna Silmic II 330µF 50V 604-1126-ND

- C806 - 470µF 16V polar electrolytic

  - Elna Silmic II 470µF 35V 604-1068-ND

- C807 - 4.7µF 50V polar electrolytic (says 10µF 50V on schematic)

  - Elna Cerafine 4.7µF 50V ELNA-72666 @ PartsConnexion

- C808 - 47µF 16V polar electrolytic

  - Elna Silmic II 47µF 25V 604-1054-ND

- C809 - 220µF 10V polar electrolytic

  - Elna Silmic II 220µF 16V 604-1114-ND

- Relay - Omron MY2Z-02DC24 (Nobody stocks this - long lead times)

Main Filter Caps

- 10,000µF 50V polar electrolytic

  - Panasonic TS-HA 10,000µF 63V P7492-ND

- Bypass Caps - Mundorf MKP 1µF 250V

  - Mundorf MKP 1µF 250V MUNDORF-71330 @ PartsConnexion

Phono Amplifier

- C401 - 1µF 25V tantalum

  - Elna Silmic II 1µF 50V 604-1117-ND

- C402 - 1µF 25V tantalum

  - Elna Silmic II 1µF 50V 604-1117-ND

- C403 - 47µF 16V polar electrolytic

  - Elna Silmic II 47µF 25V 604-1054-ND

- C404 - 47µF 16V polar electrolytic

  - Elna Silmic II 47µF 25V 604-1054-ND

- C413 - 100µF 35V polar electrolytic (axial leads)

  - Nichicon 100µF 50V axial TVX1H101MAD

- C414 - 1µF 250V stacked film capacitor - Use Panasonic ECG Metallized Polyester EF2105-ND

- C415 - 1µF 250V stacked film capacitor - Use Panasonic ECG Metallized Polyester EF2105-ND

Pre-tone Amplifier

- CE05 - 1µF 250V stacked film capacitor - Use Panasonic ECG Metallized Polyester EF2105-ND

- CE06 - 1µF 250V stacked film capacitor - Use Panasonic ECG Metallized Polyester EF2105-ND

- CE09 - 100µF 10V polar electrolytic

  - Elna Silmic II 100µF 16V 604-1110-ND

- CE10 - 100µF 10V polar electrolytic

  - Elna Silmic II 100µF 16V 604-1110-ND

- CE11 - 10µF 35V polar electrolytic

  - Elna Silmic II 10µF 50V 604-1119-ND

- CE12 - 10µF 35V polar electrolytic

  - Elna Silmic II 10µF 50V 604-1119-ND

- CE13 - 3.3µF 35V tantalum

  - WIMA 3.3µF 50V MPF capacitor

- CE14 - 3.3µF 35V tantalum

  - WIMA 3.3µF 50V MPF capacitor

- CE33 - 1.0µF 25V tantalum

  - WIMA 1.0µF 50V MPF capacitor

- CE34 - 1.0µF 25V tantalum

  - WIMA 1.0µF 50V MPF capacitor

- CE35 - 3.3µF 35V tantalum

  - WIMA 3.3µF 50V MPF capacitor

- CE36 - 3.3µF 35V tantalum

  - WIMA 3.3µF 50V MPF capacitor

- CE37 - 4.7µF 16V Bipolar electrolytic

  - Nichicon ES 4.7µF 50V NICHICON-72630 @ PartsConnexion

- CE38 - 4.7µF 16V Bipolar electrolytic

  - Nichicon ES 4.7µF 50V NICHICON-72630 @ PartsConnexion

- CE39 - 220µF 35V polar electrolytic

  - Elna Silmic II 220µF 35V 604-1066-ND